## Slide 1: Channel Estimation using PARAFAC and Sum-Rate Maximization for STAR-RIS
Vinay Kusumanchi (IMT2023608)
Rajdeep Alapati (IMT2023592)

## Slide 2
Why RIS?
6G and beyond demand for spectrum efficiency & energy efficiency
Traditional solutions: Large antenna arrays at BS → costly, high power consumption. Limited coverage in blocked areas.
Reconfigurable Intelligent Surfaces (RIS): Low-cost meta-surfaces with passive elements. Shape the wireless channel itself (not just adapt to it). Reduces coverage holes and improves spectral efficiency

## Slide 3: What is RIS?
A 2D metasurface made of many programmable passive elements.
Each element applies a controllable phase shift to the incident wave.
Works as a passive reflector.
No RF chains, no mixers, no ADCs → extremely low-cost & low-power.
Can redirect signals toward desired users by controlling phases.
Improves SNR, coverage, and spectral efficiency.
Channel estimation is challenging because RIS is passive (no receive chain)

## Slide 4: What is STAR-RIS?
Supports users on both sides of the panel (front & back).
Enables full-space coverage (360°).
Each element intelligently controls how much signal goes through (transmission) or bounces back (reflection).
Why it matters: Traditional RIS → only reflects → cannot help users behind the panel. STAR-RIS → solves this limitation → improves coverage & throughput.
STAR-RIS (Simultaneous Transmission And Reflection RIS)
Upgraded version of RIS that can transmit and reflect signals at the same time.

## Slide 5: System Model for STAR-RIS Assisted mmWave Communication
Consider a Base Station with M antennas assisting K users via a STAR-RIS with N elements.
Users are divided into: Transmission users (Kt), Reflection users (Kr)
STAR-RIS simultaneously: Reflects towards one side and transmits towards the opposite side
All users communicate with the BS only through STAR-RIS (direct link blocked).
G ∈ ℂ^{M×N} = BS → STAR-RIS channel hᵗₖ, hʳₖ ∈ ℂ^{N×1} = STAR-RIS → user channels

## Slide 6: Transmission and Reflection Coefficients
Each RIS element has two adjustable coefficients:
  Transmission:
  Reflection:
Energy conservation constraint:
Common setting used in paper (equal splitting):
STAR-RIS can direct signals toward both sides of the surface by tuning phases and amplitudes.
Phases 𝜃𝑡,𝜃𝑟​ determine the beam directions for transmission & reflection.
Amplitudes 𝛽𝑡,𝛽𝑟​ determine how much energy goes to each side.

## Slide 7: Saleh–Valenzuela mmWave Channel Model
mmWave channels modeled as sparse multipath (LoS + few NLoS paths).
BS → RIS channel:
RIS → User channels:
Steering vectors correspond to RIS UPA and BS ULA
Steering vectors specify how signals arrive/depart based on angle of arrival (AoA) and angle of departure (AoD).
Key properties:
  Sparse
  Low-rank
  Highly directional
  → exploited later in estimation.

## Slide 8: Received Signal Model (Pilots + STAR-RIS Phases)
During pilot transmission, the BS receives signals through the STAR-RIS only (direct path blocked).
Received signal at time slot i:
Components:
  G ∈ C^{M×N}: BS → STAR-RIS channel
  𝐻𝑟, 𝐻𝑡 ∈ 𝐶^{𝑁×𝐾}: RIS → users (Reflection / Transmission)
  𝛩𝑟(𝑖), 𝛩𝑡(𝑖): RIS reflection & transmission phase matrices at slot i
  𝑠𝑟(𝑖), 𝑠𝑡(𝑖): pilot symbols
  𝑛(𝑖) ∼ 𝐶𝑁(0, (𝜎^2)𝐼): noise
Key idea: RIS phases Θ𝑡(𝑖), Θ𝑟(𝑖) are changed every pilot slot introduces diversity needed for PARAFAC.
Goal: Collect received pilot signals to form a 3D tensor, enabling joint estimation of 𝐺, 𝐻𝑟​, and 𝐻𝑡​.

## Slide 9: Why PARAFAC?
The received pilots naturally form a 3-way tensor (BS antennas × pilot symbols × RIS phase patterns).
The three unknown channels G, Hr, Ht appear as three tensor factors.
RIS phase changes across pilot slots create a trilinear model:
PARAFAC/CP decomposition is built exactly for such trilinear tensors.
Identifiability: PARAFAC guarantees unique recovery of 𝐺,𝐻𝑟,𝐻𝑡 under mild conditions unlike matrix LS/MMSE.
Pilot-efficient: Needs far fewer pilots since it uses the tensor structure.
Joint estimation: Estimates all channels simultaneously (BS → RIS and RIS → Users).
Structure-exploiting: Works because RIS phases create rank-1 components in each mode.

## Slide 10: PARAFAC Tensor Model

## Slide 11: PARAFAC Algorithm (ALS Updates)
PARAFAC solves for the three channel matrices by alternating updates:
  Update Hr and Ht (RIS → users)
    Fix G and RIS phases, solve:
    Done via least squares after unfolding the tensor.
  Update Ht similarly
    Same LS structure with transmission pilots.
  Normalize each row
    Remove scaling ambiguity:
  Update G (BS → RIS)
    Fix , and solve:
  Repeat until convergence
    Typically 5–30 iterations
    NMSE decreases rapidly with SNR.
PARAFAC jointly estimates all channels using short pilots, exploiting the tensor structure created by RIS phase switching.

## Slide 12: PARAFAC Simulation Setup
Parameters used in simulation:
  BS antennas: K = 16
  RIS elements: N = 16
  Reflection users: M = 6
  Transmission users: M₁ = 6
  Pilots per user: T = 30
  RIS phase patterns (slots): P = 16
Training procedure:
  Users transmit pilots
  RIS phases change every slot
  Received signals form a K × T × P tensor
  PARAFAC decomposes tensor to estimate:
    G (BS→RIS)
    Hr (RIS → Reflection users)
    Ht (RIS → Transmission users)
Baselines compared:
  PARAFAC (our method)
  Oracle LS → Least squares using true channels (ideal but unrealistic baseline)

## Slide 13: PARAFAC Channel Estimation Results (NMSE vs SNR)
Observations:
  PARAFAC NMSE decreases significantly with SNR
  Oracle LS slightly better (as it knows true channels)
  Hr and Ht have lower NMSE since RIS-user links have fewer unknowns
  G (BS→RIS) has slightly higher NMSE because it has larger dimension (16×16) and more multipath uncertainty
PARAFAC successfully recovers all channels using short pilots and no LS overhead

## Slide 14: Why Optimization After PARAFAC?
PARAFAC only gives channel estimates (G, Hr, Ht)
But STAR-RIS has:
  Amplitude coupling: βₜ,n² + βᵣ,n² = 1
  Phase coupling: cos(φₜ,n − φᵣ,n) = 0 ⇒ |φₜ − φᵣ| = π/2 or 3π/2
This makes STAR-RIS design a non-convex optimization problem
Need to jointly optimize:
  BS beamforming (W)
  STAR-RIS transmission coefficients (θₜ)
  STAR-RIS reflection coefficients (θᵣ)
Notes: BS beamforming matrix controls how the base station weights and combines its antennas to transmit data streams toward users, and it is optimized jointly with STAR-RIS coefficients to maximize the system sum-rate.
BS beamforming matrix 𝑊controls how the base station weights and combines its antennas to transmit data streams toward users, and it is optimized jointly with STAR-RIS coefficients to maximize the system sum-rate.

## Slide 15: General Optimization Framework for STAR-RIS (PDD + BCD)
Original problem has non-convex constraints due to coupling.
Convert to Augmented Lagrangian form.
Apply alternating updates:
  Update beamforming + phases + amplitudes
  Update auxiliary variables
  Update penalty and Lagrange multipliers
PDD introduces:
  θ̃ₜ, θ̃ᵣ : auxiliary variables (decouple constraints)
  λₜ, λᵣ : Lagrange multipliers (dual variables)
  ρ : penalty factor (controls constraint enforcement)
Proved to converge to KKT optimal solution under mild conditions.
  (KKT optimal solution -> mathematically guaranteed best feasible solution for non-convex problems.)

## Slide 16: Throughput Maximization Problem
Objective:
​Constraints:
  BS transmit power
  STAR-RIS amplitude coupling: βₜ,n² + βᵣ,n² = 1
  STAR-RIS phase coupling: cos(φₜ,n − φᵣ,n) = 0
Solved using:
  WMMSE transformation → block-wise convex
  PDD (Penalty Dual Decomposition) → handles equality constraints
  BCD (Block Coordinate Descent) → solves each block efficiently

## Slide 17: Combined Workflow: PARAFAC + PDD
Step 1: Use PARAFAC to estimate (G, Hr, Ht)
Step 2: Convert PARAFAC outputs into PDD-compatible format
  G_pdd = Gᵀ
  h_pdd = [Hr_final, Ht_final]
Step 3: Initialize PDD using para_init()
Step 4: Solve:
  BS beamforming vector W
  STAR-RIS amplitudes βₜ, βᵣ
  STAR-RIS phases φₜ, φᵣ
Step 5: Obtain:
  Optimal W
  Optimal θₜ, θᵣ
  Convergence curves
  Final sum rate

## Slide 18: PDD Optimization Results: SNR = 20 dB
PDD algorithm steadily increases the sum-rate and converges near 77bit/s/Hz.
Small dip around iteration ~18 occurs due to penalty-factor update in PDD.
Phase difference curves stabilize, confirming STAR-RIS coupling constraints are satisfied.
Shows that PARAFAC-estimated channels are successfully used for sum-rate maximization.

## Slide 19: Final Observations & Key Takeaways
PARAFAC-Based Channel Estimation
  Successfully estimates all three channels (G, Hr, Ht) using short pilots.
  Achieves low NMSE, close to oracle LS performance.
  Exploits the tensor structure created by STAR-RIS phase switching.
PDD + BCD Sum-Rate Optimization
  Rapid convergence to ~80 bit/s/Hz at SNR = 20 dB.
  Handles coupled transmission–reflection constraints of STAR-RIS.
  Beamforming matrix W, amplitudes βₜ/βᵣ, and phases θₜ/θᵣ all converge smoothly.
Overall Workflow Achieved
  Channel Estimation (PARAFAC) → Channel Optimization (PDD) → Max Sum-Rate
  Shows compatibility between the two papers and correctness of implementation.

## Slide 20: References
M. Di Renzo et al., “Reconfigurable Intelligent Surfaces: Fundamentals, Solutions, and Opportunities,” arXiv, 2020.
Z. Wan, Z. Gao, F. Gao, M. D. Renzo, and M. Alouini, “Channel Estimation for RIS-Assisted Wireless Communications: Part I — Fundamentals, Solutions, and Future Opportunities,” IEEE Communications Letters, 2021.
H. Zhang et al., “Channel Estimation for STAR-RIS Assisted Multi-User Communications,” IEEE Transactions on Wireless Communications, 2022.
A. Pal, V. Yajnanarayana, and K. V. S. Hari, “Power Allocation for STAR-RIS Assisted C-V2X Systems with Discrete Phase Shifts,” IEEE VTC, 2023.
T. Hou, Y. Liu, Z. Song, X. Sun, and Y. Chen, “Coupled Phase-Shift STAR-RISs: A General Optimization Framework,” IEEE Transactions on Wireless Communications, 2023.